elektric-junkys.com

一、T-300K

1. Can control 32—65536 grey grade，software of Gamma to adjust.

2. Working with the video software LedEdit, can control regular shape and special shape light source.

3. Can connect to PC.

4. When connect to PC, can control over 300,000 pixels, when offline (not connect to PC), can control over 30,000 pixels

5. Every controller need input right IP, it is more stable.

6. There are 8 channels, every channel can control 512/1024 pixel.

7. The controller can be connect in series by cable, don’t need extra exchanger.

8. There are anti-thunder and ESD protection circuit.

9. Support single wire IC and double wire IC control, when connect to single IC lights, don’t need connect to CLK

Remark：When the controller work off line, need SD card to support.

2012 new edition CL-C300 need work with new software of LedEdit2012

二、 IC supportable：

| IC | LedEdit software item | Control pixel | Remark |
| --- | --- | --- | --- |
| LPD6803,D705,1101,6909, 6912 | T-300K-6803 | 8192 | 32 grey grade |
| LPD8806,LPD8809 | T-300K-8806 | 4096/8192 |  |
| TM1803,TM1804,TM1809,TM1812 | T-300K-TM | 4096/8192 | TM1804 and TM1809 |
| TM1903，TM1904，TM1909，TM1912 | T-300K-TM19 | 4096/8192 |  |
| UCS6909，UCS6912，UCS7009，UCS5903 | T-300K-UCS32 | 8192 |  |
| UCS1903，UCS1909，UCS1912 | T-300K-UCS256 | 4096/8192 |  |
| UCS3903 | T-300K-UCS1024 | 4096/8192 |  |
| DMX512 | T-300K-DMX | 4096/8192 | DMX512 |
| WS2801,WS2803 | T-300K-WS | 4096/8192 |  |
| WS2811 | T-300K-WS2811 | 4096/8192 |  |
| DS189 | T-300K-DS189 | 4096/8192 |  |
| TLS3001,TLS3002，TLS3008 | T-300K-TLS | 4096/8192 |  |
| P9813 | T-300K-P9813 | 4096/8192 |  |
| SM16715 | T-300K-SM16715 | 4096/8192 |  |
| SM16716 | T-300K-SM16716 | 4096/8192 |  |
| BS0901,BS0902 | T-300K-0901 | 4096/8192 |  |
| BS0815 | T-300K-0815 | 4096/8192 |  |

三、Photo：

四、System framwork

Remark：IP need write 192.168.60.178

- Connection

六、Parameter：

Memory card：

Type：SD card

Capacity：128MB—2GB

Mode：FAT

File name：*.led

Physical parameter：

Working temperature ：-30℃—85℃             Net weight：1.35KG

Power supplier：AC220V input

Power：8W

Size：L270mm×W180mm×H55mm

Notice：

Every time copy the file to SD card, need format the SD card. SD card need format to “FAT“ mode.

Before taking the SD card off, need shut off the power